## Slide 1
PROBLEM STATEMENT 26173 · ISRO / DEPARTMENT OF SPACE
iTantra
Offline Multilingual Neural Transceiver for Low-Bitrate Voice Links
10 Indian languages · 100% open-source TinyML · fully offline & air-gapped
823 MB
APK, int8 throughout
41.7%
Kannada WER (was 130%)
370 ms
voice payload air-time vs 40 s raw
Hardware-verified on two physical Android devices · 2026-09-03

## Slide 2
THE PROBLEM
Voice is too heavy for the links that need it most
In disaster and distress scenarios, voice is more inclusive than text — it reaches people regardless of literacy. But raw or compressed voice audio cannot fit through narrowband satellite, LoRa, or emergency radio channels in real time.
Chart: Seconds of air-time to transmit (log-scale gap, not to true scale)
| Raw PCM (256 kbps) | Opus codec (12 kbps) | iTantra packet (61 bytes)
Time-on-air for a 4-second utterance over a 1.2 kbps link | 853 | 40 | 0.37
99.95%
bandwidth reduction vs. raw 16 kHz PCM audio
370 ms
to transmit a full spoken sentence over a 1.2 kbps LoRa-class link, vs. 40 s for compressed Opus audio
This LoRa/satellite time-on-air figure is a feasibility calculation, not an implemented transport — see dossier §3 and §6.5 for what is and isn't built.
02

## Slide 3
SOLUTION OVERVIEW
Speech in, semantic packet across, speech out
1
Capture
Silero VAD detects a 500ms pause (Phone Mode) or PTT release, slicing the utterance.
2
Transcribe
On-device STT — SenseVoice for English, dedicated or shared IndicConformer for 9 Indic languages.
3
Transmit
≈54–61 byte packet: [LANG:xx][ALERT]<text> over Wi-Fi (working) or Bluetooth RFCOMM (built, untested end-to-end).
4
Speak
Receiver synthesizes via bundled Piper VITS (7 languages) or device TTS (3 languages); [ALERT] forces STREAM_ALARM at max volume, non-interruptible.
Two operating modes: Push-to-Talk walkie-talkie, or hands-free Phone Mode with automatic VAD-triggered dispatch.
03

## Slide 4
WHAT WE FOUND ON REAL HARDWARE
The bug wasn't the script. It was the model.
Kannada, Telugu and Tamil were transcribing at 100–130% word error rate. Our working theory was a Devanagari-vocabulary bias fixable with a Unicode script shift. Testing on real hardware disproved it.
The disproof
Marathi is already in Devanagari — zero script conversion needed — and it failed just as badly (81.9% WER). A script fix cannot explain a same-script failure.
The real cause
Binary inspection of the shipped ONNX model's own metadata confirmed it was a single shared checkpoint with no language-selection mechanism, silently defaulting to one fixed behavior for every input — even pure silence.
The fix
Sourced and hash-verified dedicated, independently-trained per-language checkpoints for Kannada, Telugu and Tamil before integrating any of them.
The verification
Two crash bugs were found and fixed only because of on-device re-testing — a missing-metadata crash and an unparseable-token crash — neither visible from a desktop build.
04

## Slide 5
ACCURACY RESULTS — HARDWARE-MEASURED
Real, measured improvement on 2 languages. Not overclaiming the rest.
Chart: Word Error Rate (%) — lower is better
| Kannada | Tamil
Before fix | 130 | 100
After fix (all tests) | 41.7 | 33.3
After fix (audio-valid tests only) | 12.5 | 0
Telugu: directionally consistent (100% → 66.7%) but only 1 of 3 tests got real audio — not claimed as proven.
Still broken — disclosed, not hidden
Gujarati · Marathi · Malayalam · Odia · Bengali
All 5 remain on the original shared STT model at 78–180% WER. No fix attempted this pass — tracked as explicit open work in dossier §6.3.
05

## Slide 6
EFFICIENCY
Shrinking the app without touching a single feature
Chart: APK size (GB)
| Before quantization | After quantization
APK size | 1.1 | 0.823
3.4×
smaller — all 7 Piper TTS voices, int8 dynamic quantization (Jacob et al., CVPR 2018)
0
crashes across a full 30-test on-device re-run after quantization
~1.8 GB
real on-device footprint after install — ONNX Runtime needs a decompressed copy; see dossier §6.4 for what was and wasn't feasible to fix
06

## Slide 7
VERIFICATION STATUS
What's proven, and what isn't yet
VERIFIED
Wi-Fi transport (UDP discovery + TCP full-duplex) — implemented and working
Bluetooth Classic RFCOMM transport — implemented, device picker built
STT/TTS pipeline benchmarked on 2 physical Android devices, 30 utterances each
Kannada + Tamil STT accuracy fix — hardware-verified
TTS quantization (3.4× smaller) — hardware-verified, zero regressions
OPEN
Two-device Wi-Fi/Bluetooth PTT round trip — not yet run end-to-end
Gujarati, Marathi, Malayalam, Odia, Bengali STT — still broken, unfixed
Telugu accuracy — directionally promising, statistically thin (n=1 clean sample)
Idle CPU / RAM figures — carried forward from an earlier pass, not re-profiled
07

## Slide 8
RESEARCH FOUNDATIONS
Built on peer-reviewed work, not marketing claims
Bhogale et al.
Vistaar: Diverse Speech Recognition Datasets for Indian Languages
Interspeech 2023
An et al.
FunAudioLLM: Voice Understanding & Generation Foundation Models
arXiv:2407.04051, 2024
Kim, Kong & Son
Conditional VAE with Adversarial Learning for End-to-End TTS (VITS)
ICML 2021
Silero Team
Silero VAD: Pre-trained Enterprise-Grade Voice Activity Detector
2024
Jacob et al.
Quantization and Training of Neural Networks for Efficient Integer-Only Inference
CVPR 2018
Bureau of Indian Standards
IS 13194:1991 — Indian Script Code for Information Interchange (ISCII)
1991
Thank you. Every number in this deck is reproducible from docs/SIH_2026_RESEARCH_DOSSIER.md and the app's own on-device benchmark harness.
08